## Slide 1: Progress Report (26th Week)
Presented by ltz
24/07/2020

## Slide 2: Environment-Independent ASL Gesture Recognition Using 60 GHz Millimeter-wave Signals
Panneer Selvam Santhalingam, Alamin Hosain, Ding Zhang, Parth Pathak, Huzefa Rangwala, Chong Tian, Raja Kushalnagar
Computer Science Department, George Mason University
Department of Science, Technology and Mathematics, Gallaudet University
[The Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies (IMWUT) 2020]

## Slide 3: MOTIVATION
An Home assistant for deaf and Hard-of-Hearing (DHH)
Alexander Toshev and Christian Szegedy, “Deeppose: Human pose estimation via deep neural networks,” in Proceedings of the IEEE conference on computer vision and pattern recognition (CVPR), IEEE, 2014, pp. 1653–1660.
Current problems
    Voice-controlled interface
    RGB, infrared: darkness,privacy
    Wearable sensors: High limitations
    CSI: SLV, low accuracy
Contributions:
    A gesture-based wake-word detection solution
    A novel deep learning approach: ASL + deep learning algorithms
    Excellent performance (87% average accuracy of sign recognition)
ASL:American Sign Language

## Slide 4: CHALLENGES
Reliable wake-word detection at any location:
  Reliable, Low-delay, everywhere
  Tolerance to other people's activities
  Solution: Spatial spectrograms + CNN
Scalable ASL sign recognition
  Home assistant —— can recognize a large number of ASL signs.
  Solution: Spectrograms+multi-task deep learning model
mmASL in uncontrolled settings
  Significant variations
  Presence of other interfering person, change of environment
  Solution: Large-scale data collection and analysis

## Slide 5: RELATED WORK
mmWave Sensing
2.4/5 GHz CSI/RSSI based systems
Vision, infrared and other modalities
System (Modality) | Device Free / Wearable (DF/W) | Other people impact | Environment impact | User position impact | Lighting impact | Wake word Detection | Non-Intrusive
RGB Camera [1,2,3,4] | DF | Low | Low | Moderate | High | No | No
Depth Camera (Kinect) [5,6,7] | DF | Low | Low | Moderate | Moderate | No | No
DeepASL[8] (Leap motion) | W | None | None | None | None | No | Yes
SignSpeaker [9](IMU) | W | None | None | None | None | No | Yes
SignFI [10] (WiFi CSI) | DF | High | High | High | None | No | Yes
mmASL (mmWave) | DF | Low to Moderate | Low | Moderate | None | Yes | Yes

## Slide 6: SYSTEM DESIGN
System overview

## Slide 7: SYSTEM DESIGN
Implementation
Fig. 1. Platform Overview
Fig. 2. Processing pipelines

## Slide 8: RECONGINZING ASL SIGNS
  Feasibility Study

## Slide 9: RECONGINZING ASL SIGNS
  ASL Phonological Properties in Spectrograms
    Repetitive + motion direction
  Multitask Learning Model
    Main task: ASL sign recognition
    Auxiliary tasks:Repetitive, motion direction
enhance

## Slide 10: WAKE WORD RECOGNITION
2 challenges:
  Timeperformance trade-off
  Presence and motion of other people
Selecting Scanning Sectors
the number of sectors to scan
the number of sectors to scan
25 beam sectors (each 5° apart)
The same coverage as the 25 sectors
Minimum overlap
main lobes + sidelobes

## Slide 11: WAKE WORD RECOGNITION
Spatial Spectrograms
X Energy
√ Spatial spectrograms

## Slide 12: EVALUATION
Scenarios and Environments
Wake-word dataset
  3700 samples, 3s/sample, 3 users, 3 different rooms
ASL sign dataset
  50 words, 12236 samples, 15 users

## Slide 13: EVALUATION
Wake-word Detection
  Wake-word selection Impact of scanning time
Machine Learning model comparison
Scenarios

## Slide 14: EVALUATION
ASL Sign Recognition
  Average sign recognition accuracy Individual user accuracy Average user accuracy

## Slide 15: ContextLoc
Indoor
Semi indoor

## Slide 16: INSPIRATION
Using mmWaves to achieve an home assistant capable of ASL recognition. The highlight is Wake-word detection.
From where I stand, the most inspiring part of the paper is that machine learning is a very powerful tool. The shortage of mmASL is too heaevy.
Combining with the work of ContextLoc, the evaluation part of the paper inspires me untrained people should be taken into account.

## Slide 17
Thanks!